## Slide 1: Unit 4, Lesson 9 Keeping You and Your Computer Safe
AOIT Computer Systems
Copyright © 2008–2013 National Academy Foundation. All rights reserved.

## Slide 2: Working with computers is relatively safe
Take precautions to minimize risk.
Understand and follow safety procedures.
Monitors and power supplies are the most hazardous devices.

## Slide 3: Electrostatic discharge (ESD) can be shocking
ESD is the rapid flow of static electricity from one object to another.
Energy is released in the form of a spark.
ESD is costly and dangerous.
ESD can interrupt power to a system.

## Slide 4: Protect yourself from ESD
Don’t become a conductor of electricity.
Damage to components can occur at low voltages.
Can you remember a time when you felt an electric shock? What do you think caused it?

## Slide 5: Ground yourself for safety’s sake
Ground is neutral:
  Not positively or negatively charged with electricity
  Connected to the earth
Grounding creates:
  An easy path for electrical current to follow
  The same electrical potential between two objects
The best sources for ground:
  AC outlet
  Metal chassis of a PC that is connected to a known ground
What do you think this universal symbol for ground is based on?
Safety Ground

## Slide 6: Wear an antistatic wrist strap
Ground yourself by wearing an antistatic wrist strap.
Attach the clip to a good ground source.
Never try to repair monitors or power supplies. Opening a monitor, especially while wearing an antistatic wrist strap, could release a lethal charge of electricity.
Why do you think an antistatic wrist strap would make a monitor or power supply release a charge of electricity?

## Slide 7: Antistatic mats slow the flow of static electricity
Antistatic mats use electrical resistance to slow the flow of static electricity across the surface of the mat.
Be sure the mat is grounded.
Use antistatic spray on the floor around the work area.
Three-layered antistatic mats reduce ESD.

## Slide 8: Power supplies retain a dangerous charge
The power supply is extremely dangerous.
Even when unplugged, the capacitor retains a potentially lethal electrical charge.
A power supply is a field replaceable unit (FRU):
  There are no serviceable parts inside.
  Replace a failed unit with a new one.

## Slide 9: You can minimize the risk of ESD damage
Store and ship computer components in antistatic bags.
Wear an antistatic wrist strap when handling components.
Remove components from the bag slowly.
Maintain humidity levels between 70% and 90%.
Never touch the electrical contacts on components.

## Slide 10: Damage from electro-magnetic interference (EMI) is recoverable
Common sources of EMI:
  High-speed digital circuits
  Radio transmitters
  Power line intercoms
  Electric motors
  Fluorescent lights
  Network cabling too close to other devices
  Electric space heaters

## Slide 11: Always follow best practices for safety
A computer’s safety documentation contains more information:
  Setup precautions
  Safe cleaning instructions
  Fire hazards during usage
  Electrocution hazards during usage
Refer to the documentation for electrical specifications.